Interview Transcript: Jeremy Giddings on the evaluation of subsurface drip irrigation systems

Stuart Bray: Jeremy what are the key aspects to take into consideration when you are doing an evaluation?

Jeremy Giddings: If the grower or the irrigator is going to do the evaluation we make it nice and simple. Record the pressures and discharges at the extremities. The extremities are the sub mains and the laterals and are generally recognised and are recommended in these quite easy tests, that the grower should do and do regularly, and also when they get a new system and make sure it operates to specifications, and then done regularly to see that the system is operating to specifications after the maintenance is done.

Stuart Bray: How important is it to do that, what happens to your performance if you don’t do it?

Jeremy Giddings: With drip irrigation it’s very important. We have found in a couple of dry years, low rainfall low water allocation and if you have a system that’s not performing as it should then you have smaller wetted rootzones ,smaller wetted area and  uneven application shows up very quickly.

Stuart Bray: What sort of performance can you expect to get?

Jeremy Giddings: It should be 95 per cent uniformity, or less than 5% variation in flow is what we are after and less than that for high value crops and crops with  small root zones like  vegetables. That’s what we should start at and maintain it around that area for the life of the system. These results are not uncommon and should happen if maintained properly.

Stuart Bray: And maintenance what are the things to consider here?

Jeremy Giddings: A couple of things are flushing, that should be looked at. People have been guilty in the past of ignoring flushing and having systems that are designed to provide adequate flushing. To flush the particles that get through to the filters it’s important to get them out of the system. Also injecting chemicals when needed depending on the problem. Chlorine and acid could be needed as well.

Stuart Bray: So when you put in the system its not set and forget, you have to continually monitor it?

Jeremy Giddings: Yes definitely, drip irrigation is a great one for reducing labour requirements but low labour doesn’t mean no labour and there’s still these issues that need to be looked at regularly.